## Slide 1
14 Oct 2026
1
Physics-Informed Neural Network
Research Update
Implementation, initial testing, and next experiments
Bonded thickness prediction in PDMS dip coating
Alexander Adams
Li Lab
October 14, 2026
Notes: Research update for October 14, 2026. Results available through October 11, 2026. All numbers in this deck come from archived PINN runs. The supplied September deck provides the theme and layout reference. No new training runs were executed for this presentation.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md

## Slide 2
14 Oct 2026
2
Introduction to physics-informed neural networks
A neural network learns a relationship between inputs and an output from examples. A PINN also uses physical rules to guide that relationship.
In this project: predict bonded thickness, enforce its physical bound, and test smoothness or mechanistic penalties where justified.
Notes: PINN means physics-informed neural network. The network is an adjustable mathematical function, and training repeatedly changes its parameters to reduce prediction errors and selected physical residuals. A loss is the numerical score used for this adjustment. Classical PINNs commonly use governing differential equations. Our present implementation is physics-constrained tabular regression: the output transform enforces the thickness bound and the default loss adds a curvature prior. No governing adsorption PDE is solved. The illustrative training loop depicts optional physics penalties conceptually, rather than asserting that all four candidate constraints are active. Generated conceptual diagram using the built-in image-generation tool; node count is schematic and is not the implemented architecture. See the later architecture slide for the exact two 16-unit layers.
Sources:
https://maziarraissi.github.io/PINNs/
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py

## Slide 3
14 Oct 2026
3
PINN implementation and initial findings
IMPLEMENTED
Compact PyTorch model predicts bonded thickness with an explicit physical bound.
Five models share each split, including two neural ablations and tree baselines.
Versioned runs preserve source, data identity, checkpoints, and per-model results.
INITIAL FINDINGS
Measured holdout: PINN RMSE 0.1223 nm. Gradient boosting performs best at 0.0649 nm.
Synthetic holdout: PINN RMSE 0.0557 nm and R² 0.905. Random forest remains stronger.
The bound guarantees physical plausibility. Initial tests have not established an accuracy benefit.
Current scope: constrained inference from measured film state
Notes: The current PINN is physics-constrained tabular regression. It does not yet solve a governing PDE or identify an adsorption mechanism. Its inputs include measured total thickness, so recipe-only process forecasting remains a separate objective.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/metrics.csv

## Slide 4
14 Oct 2026
4
Implementation changes from v0.1 to v0.2
Stage | Implementation | Reason
v0.1 baseline | 58 measured rows, three inputs Bounded tanh network and curvature prior | Establish a transparent experimental baseline
v0.1 evaluation | Grouped holdout and high-concentration test Bounded NN, standard NN, RF, and GB | Separate accuracy, bounds, and extrapolation behavior
v0.2 synthetic study | Seven inputs and audited 3k source Concentration-monotonicity ablation | Test optimization at larger scale without claiming new experiments
v0.2 physics support | Measured-velocity curvature Gated LLD mobile-layer residual | Prepare all four slide constraints with explicit activation requirements
v0.2 provenance | Dated run register and source snapshots Published code, data, results, and checkpoints | Make each experiment reviewable and reproducible
Five archived runs cover the measured baseline, extrapolation, and synthetic ablation
Notes: Implementation completed October 11, 2026. v0.1 runs predate prospective execution timestamps. v0.2 adds timestamped lifecycle records and seven-input synthetic benchmarks. The measured rerun reproduces v0.1 results. The code and artifacts are published on codex/pinn-physics-and-run-tracking with draft PR #6.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/CHANGELOG.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/pull/6

## Slide 5
14 Oct 2026
5
Measured and synthetic data audits
MEASURED BASELINE
58
Hexane observations
16 concentration levels
Three predictors and one target
All 58 rows pass the numerical
and thickness-bound checks.
SYNTHETIC SOURCE
Audit check | Rows
Raw combined source | 3,000
Nonpositive concentration | 182
Nonpositive total thickness | 6
Bonded greater than total | 113
Unique excluded rows | 192
Retained rows | 2,808
Exclusion reasons overlap. Preserve the raw source and original row IDs
Notes: Counts overlap: 182+6+113 is not the number excluded. The union of invalid checks is 192, leaving 2808. The default physical checks also reject negative bonded values, negative layer inputs, missing/nonfinite values and invalid log inputs. There were no additional excluded rows under these checks for this benchmark. The combined synthetic source remains byte-identical to its original snapshot. Parent-row provenance is unavailable.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/datasets/provenance.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/data_audit.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 6
14 Oct 2026
6
Feature choices and preprocessing
Feature group | Measured run | Synthetic run
Film and process state | Concentration Uncoated layer Total thickness | Same three measured-state inputs
Solvent descriptors | Unavailable in the four-column workbook | Polarity, viscosity Boiling point, surface tension
Concentration transform | Natural logarithm | Natural logarithm
Input scaling | Training-only standardization | Training-only standardization
Output | Bonded thickness in nm | Bonded thickness in nm
Confirm concentration units and measurement timing before mechanistic interpretation
Notes: Recorded concentration spans 0.02 to 10 in the measured CSV, a 500-fold range. A natural log reduces scale imbalance. The source labels say g/mL, but high values and differences between workbooks and derived tables require lab confirmation. StandardScaler fits the training rows only. Bonded thickness never enters the input set. Total thickness is also the raw output envelope and is required at inference. Solvent descriptors have only three solvent-associated combinations in the synthetic data.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md

## Slide 7
14 Oct 2026
7
Compact network and bounded bonded thickness
3 or 7
inputs
16 + 16
tanh
Bounded
bonded hB
Derivative
penalties
NETWORK DETAILS
Two hidden layers, 16 units each
One output logit
353 parameters with three inputs
417 parameters with seven inputs
Tanh supports second derivatives
PHYSICAL OUTPUT
Raw measured total thickness
defines the output bound
Notes: Architecture: d inputs, Linear(d,16), tanh, Linear(16,16), tanh, Linear(16,1), then sigmoid multiplied by raw measured total thickness. Parameter count is 16d+16+272+17, giving 353 for d=3 and 417 for d=7. Xavier-uniform weights and zero biases initialize the network. A positive measured total is required in data loading. Finite logits approach the endpoints asymptotically. The standard-NN ablation retains the same hidden layers but uses a linear unbounded output. Diagram structure is reused from slide 15 of the provided reference.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md

## Slide 8
14 Oct 2026
8
Loss terms and initial coefficients
Term | Definition or behavior | Initial coefficient
Data | Mean squared error in bonded thickness Normalize by training target standard deviation | 1
Curvature | Mean squared diagonal second derivative With respect to standardized transformed inputs | 0.001
Monotonicity | Penalize partial derivatives with the wrong sign Separate positive-concentration ablation | 0 default 0.01 ablation
Velocity curvature | Second derivative with respect to measured withdrawal velocity input | 0 in current runs
LLD residual | Compare predicted dry mobile thickness with the eligible hydrodynamic estimate | 0 in current runs
The hard thickness bound comes from the output transform, not a penalty weight
Notes: Ldata = mean(((hB_hat-hB)/sy)^2), with sy the population standard deviation of training targets floored at 1e-6. Lsmooth is a diagonal-Hessian curvature prior of hB_hat/sy in standardized/log-transformed coordinates, not a full Hessian norm. Differentiate the total-thickness envelope too. v0.2 evaluates derivative terms on up to 256 deterministic training-row samples per epoch. No arbitrary Cartesian collocation is added. Monotonic penalties are local soft penalties on normalized gradients. Weight decay is an optimizer parameter, separate from the displayed loss.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic_monotonic.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py

## Slide 9
14 Oct 2026
9
Mathematical definitions of the loss terms
Each loss scores a different kind of error. The coefficients set how strongly training responds to each score.
DATA FIT
Prediction error relative to measured bonded thickness
INPUT SMOOTHNESS
Penalizes curvature in each recorded input
MONOTONICITY
Penalizes slopes that oppose the selected sign
VELOCITY SMOOTHNESS
Penalizes curvature in the standardized velocity input
z: standardized inputs sy: training target scale
n: data rows m: derivative rows d: input count
Notes: The symbols reproduce the implementation exactly. q is predicted bonded thickness divided by s_y, the population standard deviation of training targets with floor 1e-6 nm. n is the count of training data rows, m is the count selected for derivatives (up to 256 per epoch), and d is the number of inputs. z contains standardized transformed predictors, including log concentration. J is the configured set of monotonic features and s_j is their selected direction, positive or negative. z_U is the standardized withdrawal-velocity coordinate; this is not an unscaled SI-velocity derivative. All derivatives include the total-thickness output envelope. Curvature is a diagonal Hessian penalty, not the full Hessian norm. Monotonicity is a soft local penalty. No derivative penalty is evaluated on the held-out test. LaTeX sources for all equations are retained in assets/equations.tex.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py

## Slide 10
14 Oct 2026
10
Status of the four proposed physics constraints
Constraint | Implementation | Current status
Thickness bound | Sigmoid output multiplied by measured total thickness | ACTIVE Hard guarantee
Velocity smoothness | Penalty on velocity curvature | AVAILABLE No measured velocity in current tables
Monotonic trends | Configurable derivative-sign loss Training-only trend diagnostics | TESTED FOR CONCENTRATION Viscosity remains unconstrained
Hydrodynamic scaling | LLD residual on the dry mobile layer Explicit regime and conversion checks | AVAILABLE Required physical measurements missing
The general curvature prior smooths the recorded inputs. It does not demonstrate smoothness in an unmeasured velocity.
Implemented support and experimentally justified activation are separate decisions
Notes: The provided overview slide 15 lists these four candidate constraints. The concentration ablation sets a positive sign as an exploratory hypothesis, not a validated law. Three solvent-associated viscosity values cannot isolate a viscosity mechanism. Velocity smoothness and the hydrodynamic residual fail explicitly when enabled without necessary data. The nonnegative mobile layer follows from the bound, so it is not counted as an independent constraint.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/PHYSICS_CONSTRAINTS.md

## Slide 11
14 Oct 2026
11
Hydrodynamic residual and activation requirements
η: viscosity U: withdrawal velocity
γ: surface tension ρ: density
MEASURED INPUTS
Velocity, solution viscosity, surface tension,
and solution density
Independent wet-to-dry conversion factor
VALIDITY CHECKS
Flat-plate, Newtonian, eligible regime
Explicit per-row applicability flag
Capillary number below 0.01
A: eligible rows fdry: independent dry conversion sy: training target scale
The residual regularizes the mobile layer. Bonded adsorption needs separate physics
Notes: The 0.9458 classical plate coefficient is supported by the JFM two-liquid dip-coating paper. U in mm/s converts by 1e-3 to m/s, viscosity cP by 1e-3 to Pa*s, surface tension mN/m by 1e-3 to N/m, and wet thickness m to nm by 1e9. rho is kg/m3 and g=9.81 m/s2. The conversion factor must be independent of the bonded target, positive and <=1. The Ca threshold is a conservative starting gate, not a universal regime guarantee. Geometry, wetting, evaporation and interface validity are supplied by the lab flag. Current runs leave this loss off.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_measured_physics.example.json
https://www.cambridge.org/core/journals/journal-of-fluid-mechanics/article/dipcoating-flow-in-the-presence-of-two-immiscible-liquids/CB484EB73B1903B5933AB087847C642E

## Slide 12
14 Oct 2026
12
Training configuration and matched baselines
Setting | Initial choice
Optimizer | Adam
Learning rate | 0.001
Weight decay | 0.0001
Maximum epochs | 1,500
Validation patience | 150 epochs
Gradient clipping | Norm = 10
Derivative sample | Up to 256 training rows
Initialization | Xavier / zero biases
Reproducibility | Seed 42, CPU
NEURAL COMPARISONS
PINN: hard bound plus curvature regularization.
Bounded NN: same output bound, with physics penalties off.
Standard NN: same hidden layers and optimizer, with a linear output.
TREE BASELINES
RF: 300 trees, minimum leaf size 2
GB: 100 trees, depth 2, learning rate 0.05
Validation chooses neural checkpoints. Fixed tree settings receive no test-driven tuning
Notes: All neural models use full-batch supervised training, training-only preprocessing and normalized data loss. Adam uses coupled weight decay as implemented by torch.optim.Adam. Torch uses float32 tensors, one CPU thread and deterministic operations. Early stopping counts epochs without validation improvement >1e-7 and restores the selected state. v0.2 experimental PINN selects epoch 76 and stops after epoch 226. Synthetic PINNs select epoch 1500. RF and GB settings are fixed untuned baselines.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/train.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/run_record.json

## Slide 13
14 Oct 2026
13
Evaluation splits and interpretation
Run | Training | Validation | Test
Measured concentration groups | 28 | 12 | 18
Measured high-concentration holdout | 36 | 12 | 10
Synthetic concentration groups | 1,959 | 407 | 442
MEASURED GENERALIZATION
Hold out entire concentration levels.
The extrapolation test reserves
3, 5, 7, and 10 in recorded units.
SYNTHETIC GENERALIZATION
Synthetic parent IDs are unavailable.
Exact concentration grouping cannot
prove independent source experiments.
Compare models within each shared split. Do not compare scores across protocols
Notes: Grouped split reserves 20% of concentration groups for test and then 20% of remaining groups for validation, so row proportions vary. Extrapolation reserves the largest four of sixteen measured concentration levels. The v0.2 synthetic default and monotonicity runs use identical retained rows and partitions. Existing historical stratified-CV RF scores in the September deck use other protocols and are not direct competitors for these single-split results. True independent batches/specimens should replace concentration as the grouping unit when available.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/train.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/splits.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/splits.csv

## Slide 14
14 Oct 2026
14
Initial measured-data benchmark
58 observations, three inputs, 18 held-out rows
Chart: Held-out RMSE (nm)
| PINN | Bounded | Standard | RF | GB
RMSE (nm) | 0.12225 | 0.12241 | 0.21195 | 0.06698 | 0.064933
Model | RMSE (nm) | R²
PINN | 0.1223 | -0.392
Bounded NN | 0.1224 | -0.395
Standard NN | 0.2119 | -3.183
Random forest | 0.0670 | 0.582
Gradient boosting | 0.0649 | 0.607
PINN MAE: 0.1117 nm. All models: 0% observed bound violations.
Gradient boosting and random forest outperform the initial neural models
Notes: v0.2 experimental grouped run reproduces the original measured grouped results. Metrics refer only to 18 test observations on held-out concentration levels. PINN MAE 0.111693 nm, RMSE 0.122251 nm, R2 -0.391624. GB MAE 0.055622 nm, RMSE 0.064933 nm, R2 0.607406. All five observed violation fractions are zero, but only bounded outputs guarantee the inequality. Negative R2 means worse than a constant test-set-mean predictor on this small split. This is not evidence that neural models cannot work after a separate validation-based study.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/metrics.csv

## Slide 15
14 Oct 2026
15
Measured high-concentration extrapolation
Chart: Bonded thickness at held-out concentrations
| 3 | 3 | 3 | 5 | 5 | 5 | 7 | 7 | 7 | 10
Observed | 0.55 | 0.56 | 0.57 | 0.56 | 0.55 | 0.55 | 0.5 | 0.53 | 0.52 | 0.51
PINN | 0.56907 | 0.56412 | 0.56814 | 0.72507 | 0.73034 | 0.7443 | 1.31 | 1.2969 | 1.3547 | 1.8387
RF | 0.57942 | 0.5801 | 0.57942 | 0.57942 | 0.5801 | 0.5801 | 0.49937 | 0.49937 | 0.49937 | 0.57092
Model | RMSE (nm)
PINN | 0.6168
Bounded NN | 0.6115
Standard NN | 0.1042
Random forest | 0.0294
Gradient boosting | 0.0296
10 measured test rows
All models have negative R²
PINN R²: −759.817
The PINN satisfies the bound while its error grows at unseen high concentrations
Notes: Legacy v0.1 extrapolation uses 36 training, 12 validation and 10 test rows. RF RMSE is 0.029366 and R2 -0.724719, GB RMSE 0.029637 and R2 -0.756752. Test bonded values range only 0.50 to 0.57 nm, so R2 is highly sensitive to small error. At recorded concentration 10 the PINN predicts about 1.839 nm for observed 0.51 nm, still below measured total 13.18 nm. Multiplication by increasing total may contribute to error when the learned fraction extrapolates poorly. This is a plausible explanation, not a proven mechanism. No subsequent tuning used this test.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/predictions.csv

## Slide 16
14 Oct 2026
16
Seven-input synthetic benchmark
2,808 retained rows, seven inputs, 442 held-out rows
Chart: Synthetic holdout RMSE (nm)
| PINN | Bounded | Standard | RF | GB
RMSE (nm) | 0.055718 | 0.055137 | 0.054133 | 0.035903 | 0.074783
Model | RMSE (nm) | R²
PINN | 0.0557 | 0.905
Bounded NN | 0.0551 | 0.907
Standard NN | 0.0541 | 0.911
Random forest | 0.0359 | 0.961
Gradient boosting | 0.0748 | 0.829
PINN MAE: 0.0436 nm. All models: 0% observed bound violations.
Synthetic PINN R² reaches 0.905. Random forest still gives the lowest error
Notes: PINN MAE 0.043595 nm, RMSE 0.055718 nm, R2 0.905199. RF MAE 0.020570 nm, RMSE 0.035903 nm, R2 0.960637. This is one synthetic-distribution holdout with seed 42. It cannot be compared as an accuracy improvement over the 58-row measured study because data, feature count, regime composition and test distribution differ. Synthetic siblings and generator statistics may leak without parent provenance. All test violation fractions are zero.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 17
14 Oct 2026
17
Synthetic holdout parity: PINN and random forest
Chart: PINN
Ideal prediction | 0.15 | 1.15
Chart: Random forest
Ideal prediction | 0.15 | 1.15
Both plots use all 442 identical test rows and matching axes
Notes: Each point is one archived held-out synthetic row. Axes are equal in both panels, from 0.15 to 1.15 nm, and the gray diagonal marks predicted=observed. Repeated or overlapping points are not jittered. The raw dataset contains synthetic replicates, so apparent point density does not indicate independent experimental replication. Random forest predictions lie closer to the diagonal on this run.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/predictions.csv

## Slide 18
14 Oct 2026
18
Concentration-monotonicity ablation
PINN run | RMSE (nm) | R² | Negative local concentration slope
Default curvature prior | 0.055718 | 0.905199 | 43.44%
Positive concentration penalty | 0.056009 | 0.904208 | 40.99%
Chart: Training rows with negative concentration partial derivative
| Pooled | 0.377 cP | 0.423 cP | 0.68 cP
Default | 0.43441 | 0.86553 | 0.23169 | 0.31365
Concentration penalty | 0.4099 | 0.82386 | 0.20628 | 0.30184
The penalty reduces some negative slopes but slightly worsens held-out error
Notes: Ablation sets monotonic_weight=.01 and sign +1 on concentration only. Architecture, seed, preprocessing, split and other weights match the default run. Fractions come from training-only gradients, not test data. Default pooled negative fraction .434405, ablation .409903. Cohorts are solvent-associated viscosities .377, .423 and .68 cP. In the .377 cohort the training Spearman association is only .100041. A soft local penalty does not guarantee global monotonicity, and synthetic correlation is not evidence of causal chemistry. Keep this hypothesis separate from the default.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/training_trend_diagnostics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_concentration_monotonic/training_trend_diagnostics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic_monotonic.json

## Slide 19
14 Oct 2026
19
Training histories and selected checkpoints
Chart: Measured PINN
| 1 | 6 | 11 | 16 | 21 | 26 | 31 | 36 | 41 | 46 | 51 | 56 | 61 | 66 | 71 | 76 | 81 | 86 | 91 | 96 | 101 | 106 | 111 | 116 | 121 | 126 | 131 | 136 | 141 | 146 | 151 | 156 | 161 | 166 | 171 | 176 | 181 | 186 | 191 | 196 | 201 | 206 | 211 | 216 | 221 | 226
Training data loss | 2.8329 | 2.7629 | 2.6793 | 2.5812 | 2.4682 | 2.3391 | 2.1929 | 2.0282 | 1.8431 | 1.634 | 1.3941 | 1.112 | 0.7692 | 0.34929 | -0.059142 | -0.19057 | -0.3231 | -0.54496 | -0.53727 | -0.51981 | -0.57602 | -0.59848 | -0.6224 | -0.64753 | -0.6558 | -0.66734 | -0.68086 | -0.69128 | -0.70185 | -0.7111 | -0.71964 | -0.72854 | -0.73709 | -0.7453 | -0.75314 | -0.76056 | -0.76768 | -0.77446 | -0.78092 | -0.7871 | -0.79303 | -0.79874 | -0.80421 | -0.80944 | -0.81442 | -0.81917
Validation data loss | 3.0567 | 3.0069 | 2.9467 | 2.8746 | 2.7894 | 2.6892 | 2.5717 | 2.4334 | 2.2696 | 2.0738 | 1.8375 | 1.5488 | 1.188 | 0.72026 | 0.14791 | -0.095871 | -0.055884 | 0.11097 | 0.28341 | 0.29304 | 0.21353 | 0.15589 | 0.14449 | 0.15743 | 0.1578 | 0.13175 | 0.10198 | 0.089863 | 0.09382 | 0.099395 | 0.096012 | 0.085313 | 0.074578 | 0.067259 | 0.061684 | 0.055321 | 0.048109 | 0.041601 | 0.036434 | 0.031761 | 0.026596 | 0.020911 | 0.015315 | 0.010168 | 0.0053384 | 0.00059528
Chart: Synthetic PINN
Selected epoch 76
Training stopped at epoch 226
Selected epoch 1,500
Training reached the configured limit
A validation-based optimization-budget study remains a next step
Notes: Charts use log10 of archived normalized data-loss and validation-loss histories. Log display retains the full initial and final loss ranges without clipping. A value of -1 means normalized MSE=0.1, 0 means 1, and 3 means 1000. The normalization uses each run training target standard deviation, so charts describe within-run optimization rather than comparing absolute nm errors across datasets. Figure samples every fifth measured epoch and every 25th synthetic epoch plus endpoints. All three synthetic neural models selected epoch 1500. Test results never select epochs.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/pinn_history.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/pinn_history.csv

## Slide 20
14 Oct 2026
20
Architecture choices from the literature
Architecture | Relevant work | Decision for this project
Compact tanh MLP | Raissi et al., 2019 | Initial backbone for differentiable small-data constrained regression
Modified or gated MLP | Wang et al., 2021 Gradient pathologies | Next candidate if diagnostics show conflicting loss gradients
Fourier-feature PINN | Wang et al., 2021 Eigenvector bias | Test only with evidence of multiscale response rather than measurement noise
Bayesian PINN | Yang et al., 2021 B-PINNs | Consider after auditing replicate noise and checking uncertainty calibration
DeepONet / FNO | Lu et al., 2021 Li et al., ICLR 2021 | Defer until trajectories, profiles, or families of field solutions exist
The current scalar table supports a compact network before operator-learning models
Notes: Literature is methodological background rather than evidence of a PDMS adsorption law. The sigmoid envelope is our algebraic project parameterization, not a reproduction of Lu et al. hPINN augmented-Lagrangian optimization. Operator architectures need function-valued input/output structure absent from three/seven scalar predictors. Full verified source links appear on the reference slide and in the repository literature review.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/LITERATURE_REVIEW.md
https://doi.org/10.1016/j.jcp.2018.10.045
https://arxiv.org/abs/2001.04536
https://arxiv.org/abs/2012.10047
https://arxiv.org/abs/2003.06097
https://www.nature.com/articles/s42256-021-00302-5
https://arxiv.org/abs/2010.08895

## Slide 21
14 Oct 2026
21
Recorded experiments and reproducibility
Run | Version | Start, Oct 11 (EDT) | PINN RMSE
Measured grouped baseline | 0.1.0 | Unknown legacy time | 0.122251 nm
Measured extrapolation | 0.1.0 | Unknown legacy time | 0.616773 nm
Synthetic grouped benchmark | 0.2.0 | 11:42:34 | 0.055718 nm
Measured grouped rerun | 0.2.0 | 11:44:41 | 0.122251 nm
Synthetic concentration ablation | 0.2.0 | 11:45:28 | 0.056009 nm
Each new run stores execution times, per-model settings and results, exact source/configuration, data and artifact hashes, split IDs, and saved checkpoints.
Ten integrity tests passed. All 111 archived artifacts match their published Git bytes
Notes: Legacy start/end execution times were never recorded. Their file modification times are approximate archival evidence and are not presented as execution timestamps. Three v0.2 runs capture UTC and America/New_York times prospectively. Code version plus exact source hash and source snapshot is authoritative when the worktree differed from its Git base. The v0.2 Git-status path-scope bug was corrected and annotated without changing scientific results. Byte-preserving attributes and a later Git renormalization repair preserve archive hashes. Source, models, raw/processed identity, predictions and runs are published on branch codex/pinn-physics-and-run-tracking, draft PR #6. Future runs record automatically but require a commit/push to publish.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/run_tracking.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/verify_runs.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/pull/6

## Slide 22
14 Oct 2026
22
What initial testing establishes
SUPPORTED FINDINGS
The bounded architecture guarantees physically valid thickness predictions for valid totals.
The measured PINN trails tree models on the initial concentration-group holdout.
The synthetic PINN fits the represented distribution, while random forest remains stronger.
LIMITS ON INTERPRETATION
Total thickness is a measured input. Recipe-only prediction needs a separate model design.
Synthetic parent provenance and independent experimental batches remain unresolved.
No calibrated uncertainty, governing PDE, or identified adsorption mechanism is established.
Physics plausibility and predictive accuracy require separate evidence
Notes: These are single-seed, single-split exploratory tests. Test-set concentration ranges, solvent combinations, independent replicate count, source-unit ambiguity and target algebraic coupling limit causal and deployment claims. The high-concentration test demonstrates that staying within a bound does not ensure accurate extrapolation. No accuracy benefit from default curvature or the tested positive monotonicity penalty is established here.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/INITIAL_RESULTS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 23
14 Oct 2026
23
Next experiments and decision criteria
Workstream | Next action | Evidence to proceed
Data and units | Confirm units and measurement timing Add batch IDs and replicate error | Verified units and independent groups
Missing physics | Measure velocity, rheology and density Validate regime and dry conversion | Eligible regime and independent dry conversion
Validation | Repeat seeds and grouped experimental CV Reserve new independent test experiments | Stable error on an untouched measured test
Architecture and losses | Test compact adsorption or saturation priors Tune only on training/validation | Gain over bounded NN with a frozen test
Data efficiency | Augment after splitting measured parents Use fixed measured-test learning curves | Gain on measured tests with known training parents
Immediate priority: validate measurements and splits before stronger physics claims
Notes: No new numerical result is promised by these next steps. Proposed saturation or adsorption parameterizations need independent physical evidence and identifiability checks. Velocity/LLD terms activate only after their measurement contract is met. A defensible augmentation study splits measured experiments before generating synthetic training rows. Test remains frozen, including when considering loss balancing, Bayesian uncertainty or Fourier features. Questions for the lab: what are the true concentration units, what measurements exist for velocity/density, what identifies independent samples, and when are total/uncoated thickness measured?
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/PHYSICS_CONSTRAINTS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 24
14 Oct 2026
24
References and archived evidence
PHYSICS-INFORMED ARCHITECTURES
Raissi, Perdikaris & Karniadakis (2019)
Physics-informed neural networks, JCP
DOI: 10.1016/j.jcp.2018.10.045
Lu et al. (2021)
Hard constraints for inverse design
arXiv: 2102.04626
Wang, Teng & Perdikaris (2021)
Gradient flow pathologies in PINNs
DOI: 10.1137/20M1318043
Wang, Wang & Perdikaris (2021)
Fourier-feature eigenvector bias
DOI: 10.1016/j.cma.2021.113938
Yang, Meng & Karniadakis (2021)
B-PINNs for noisy forward/inverse problems
DOI: 10.1016/j.jcp.2020.109913
Lu et al. (2021)
DeepONet, Nature Machine Intelligence
DOI: 10.1038/s42256-021-00302-5
Li et al. (ICLR 2021)
Fourier Neural Operator
arXiv: 2010.08895
CODE AND RESULTS
GitHub: aadams2006 / Pitt-ML-MSE-Project
PINN folder and experiment register
Draft pull request #6
Results through October 11, 2026. Full sources and numerical details are in speaker notes.
Notes: Architecture citations are the reviewed papers, not newly generated research claims. The deck uses the five archived PINN runs and the requested reference theme. The classical LLD coefficient and applicability discussion are sourced on slide 9. Data, code, run manifests and predictions identify all quantitative figures. Meeting date: October 14, 2026. Result cutoff: October 11, 2026.
Sources:
https://doi.org/10.1016/j.jcp.2018.10.045
https://arxiv.org/abs/2102.04626
https://doi.org/10.1137/20M1318043
https://doi.org/10.1016/j.cma.2021.113938
https://doi.org/10.1016/j.jcp.2020.109913
https://www.nature.com/articles/s42256-021-00302-5
https://arxiv.org/abs/2010.08895
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/LITERATURE_REVIEW.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md