## Slide 1
14 Oct 2026
1
Physics-Informed Neural Network
Research Update
Implementation, initial testing, and next experiments
Bonded thickness prediction in PDMS dip coating
Alexander Adams
Li Lab
October 14, 2026
Notes: SPEAKER SCRIPT
Today I will walk through how we implemented a physics-informed model for bonded thickness in PDMS dip coating, what the first tests show, and what we plan to do next. The practical goal is to predict bonded thickness while incorporating physical restrictions we already know. We are evaluating two separate questions: whether a prediction respects those restrictions, and whether it is accurate on measurements the model has not seen. The numerical results come from runs archived through October 11. The data-preparation status reflects our October 14 update: values needed for every proposed loss term are available, but some datasets still need aggregation and preprocessing.
TRANSITION
First, I will explain what a physics-informed neural network is without assuming an ML background.
TECHNICAL REFERENCE AND SOURCES
Research update for October 14, 2026. Results available through October 11, 2026. All numbers in this deck come from archived PINN runs. The supplied September deck provides the theme and layout reference. No new training runs were executed for this presentation.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md

## Slide 2
14 Oct 2026
2
Introduction to physics-informed neural networks
A neural network learns a relationship between inputs and an output from examples. A PINN also uses physical rules to guide that relationship.
In this project: predict bonded thickness, enforce its physical bound, and test smoothness or mechanistic penalties where justified.
Notes: SPEAKER SCRIPT
Think of a neural network as an adjustable mathematical relationship between measured inputs and an output. Its parameters are numerical coefficients, rather than separately identified physical constants. Training means repeatedly adjusting those coefficients so predictions agree better with examples. A physics-informed neural network, or PINN, also uses physical knowledge to guide the relationship. Following the diagram, inputs enter the network, the network predicts bonded thickness, and we score agreement with measurements and selected physical rules. Those scores guide the next parameter update. A loss is simply the numerical error score that training tries to reduce. Classical PINNs often use governing differential equations. Our current model uses a thickness bound and smoothness penalties; it does not solve an established governing adsorption equation. The diagram illustrates the training idea, while the later architecture slide shows the actual network size.
IF ASKED
A rule can enter as a hard restriction that every output must satisfy, or as a soft penalty that discourages undesirable behavior. Our thickness bound is hard. The derivative penalties are soft.
TRANSITION
With that framework, here is what we have implemented and what the initial evidence says.
TECHNICAL REFERENCE AND SOURCES
PINN means physics-informed neural network. The network is an adjustable mathematical function, and training repeatedly changes its parameters to reduce prediction errors and selected physical residuals. A loss is the numerical score used for this adjustment. Classical PINNs commonly use governing differential equations. Our present implementation is physics-constrained tabular regression: the output transform enforces the thickness bound and the default loss adds a curvature prior. No governing adsorption PDE is solved. The illustrative training loop depicts optional physics penalties conceptually, rather than asserting that all four candidate constraints are active. Generated conceptual diagram using the built-in image-generation tool; node count is schematic and is not the implemented architecture. See the later architecture slide for the exact two 16-unit layers.
Sources:
https://maziarraissi.github.io/PINNs/
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py

## Slide 3
14 Oct 2026
3
PINN implementation and initial findings
IMPLEMENTED
Compact PyTorch model predicts bonded thickness with an explicit physical bound.
Five models share each split, including two neural ablations and tree baselines.
Versioned runs preserve source, data identity, checkpoints, and per-model results.
INITIAL FINDINGS
Measured holdout: PINN RMSE 0.1223 nm. Gradient boosting performs best at 0.0649 nm.
Synthetic holdout: PINN RMSE 0.0557 nm and R² 0.905. Random forest remains stronger.
The bound guarantees physical plausibility. Initial tests have not established an accuracy benefit.
Current scope: constrained inference from measured film state
Notes: SPEAKER SCRIPT
We now have a compact network, comparison models, and a record of each experiment. The comparison models tell us whether the added physics actually helps, rather than assuming a more sophisticated model must be better. On measured data, the PINN's root mean squared error is about 0.122 nanometers, while gradient boosting reaches about 0.065 nanometers on the same held-out rows. Lower error is better. On the synthetic test, the PINN reaches about 0.056 nanometers, but random forest still performs better. These are different datasets and test distributions, so the lower synthetic error is not evidence that experimental performance improved. The strongest established property is the thickness bound. The current tests do not yet establish an accuracy benefit from the added penalties.
IF ASKED
A baseline is a reference model. An ablation removes or changes one component so we can investigate what that component contributes.
TRANSITION
The implementation developed in several stages, which this next slide summarizes.
TECHNICAL REFERENCE AND SOURCES
The current PINN is physics-constrained tabular regression. It does not yet solve a governing PDE or identify an adsorption mechanism. Its inputs include measured total thickness, so recipe-only process forecasting remains a separate objective.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/metrics.csv

## Slide 4
14 Oct 2026
4
Implementation changes from v0.1 to v0.2
Stage | Implementation | Reason
v0.1 baseline | 58 measured rows, three inputs Bounded tanh network and curvature prior | Establish a transparent experimental baseline
v0.1 evaluation | Grouped holdout and high-concentration test Bounded NN, standard NN, RF, and GB | Separate accuracy, bounds, and extrapolation behavior
v0.2 synthetic study | Seven inputs and audited 3k source Concentration-monotonicity ablation | Test optimization at larger scale without claiming new experiments
v0.2 physics support | Measured-velocity curvature Gated LLD mobile-layer residual | Prepare all four slide constraints with explicit activation requirements
v0.2 provenance | Dated run register and source snapshots Published code, data, results, and checkpoints | Make each experiment reviewable and reproducible
Five archived runs cover the measured baseline, extrapolation, and synthetic ablation
Notes: SPEAKER SCRIPT
Version 0.1 established a measured-data baseline with three inputs, a bounded neural network, and a smoothness penalty. We then evaluated it against simpler alternatives and checked behavior at concentrations beyond the training range. Version 0.2 added the larger synthetic study with seven inputs, an exploratory concentration-monotonicity test, and support for the remaining physics terms. Monotonicity means testing whether the prediction should consistently increase or decrease as a chosen input changes. We also added a dated run register and saved the exact code, configurations, and results. The versions identify implementation changes; they do not imply that every new version is more accurate. The remaining loss inputs are available, and the next integration step is to aggregate and preprocess their datasets.
TRANSITION
Before discussing the model itself, I will distinguish the measured and synthetic data used in these tests.
TECHNICAL REFERENCE AND SOURCES
Implementation completed October 11, 2026. v0.1 runs predate prospective execution timestamps. v0.2 adds timestamped lifecycle records and seven-input synthetic benchmarks. The measured rerun reproduces v0.1 results. The code and artifacts are published on codex/pinn-physics-and-run-tracking with draft PR #6.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/CHANGELOG.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/pull/6

## Slide 5
14 Oct 2026
5
Measured and synthetic data audits
MEASURED BASELINE
58
Hexane observations
16 concentration levels
Three predictors and one target
All 58 rows pass the numerical
and thickness-bound checks.
SYNTHETIC SOURCE
Audit check | Rows
Raw combined source | 3,000
Nonpositive concentration | 182
Nonpositive total thickness | 6
Bonded greater than total | 113
Unique excluded rows | 192
Retained rows | 2,808
Exclusion reasons overlap. Preserve the raw source and original row IDs
Notes: SPEAKER SCRIPT
The measured baseline contains 58 observations and 16 concentration levels. That is a small dataset for estimating a flexible relationship. The synthetic source contains 3,000 rows, which are generated examples rather than 3,000 new laboratory measurements. We screened the source for invalid numerical or physical values. Some rows have nonpositive concentration or total thickness, and some have bonded thickness greater than total thickness. A row can fail more than one check, so the exclusion counts overlap. We excluded 192 unique rows and retained 2,808. This screening makes the data consistent with our input and output requirements; it does not establish experimental independence or validate the synthetic generator. We also preserve original row identities so exclusions remain traceable.
IF ASKED
Synthetic data can help test optimization and represented relationships, but performance on synthetic examples needs separate confirmation on independent measurements.
TRANSITION
The next slide shows exactly which quantities each archived model received as inputs.
TECHNICAL REFERENCE AND SOURCES
Counts overlap: 182+6+113 is not the number excluded. The union of invalid checks is 192, leaving 2808. The default physical checks also reject negative bonded values, negative layer inputs, missing/nonfinite values and invalid log inputs. There were no additional excluded rows under these checks for this benchmark. The combined synthetic source remains byte-identical to its original snapshot. Parent-row provenance is unavailable.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/datasets/provenance.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/data_audit.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 6
14 Oct 2026
6
Feature choices and preprocessing
Feature group | Measured run | Synthetic run
Film and process state | Concentration Uncoated layer Total thickness | Same three measured-state inputs
Solvent descriptors | Unavailable in the four-column workbook | Polarity, viscosity Boiling point, surface tension
Concentration transform | Natural logarithm | Natural logarithm
Input scaling | Training-only standardization | Training-only standardization
Output | Bonded thickness in nm | Bonded thickness in nm
Confirm concentration units and measurement timing before mechanistic interpretation
Notes: SPEAKER SCRIPT
A feature is an input quantity given to the model. The measured run used concentration, uncoated-layer thickness, and total thickness. The synthetic run added four solvent descriptors. This table describes the prepared tables used in the reported runs, rather than the full set of values now available across our datasets. Bonded thickness is the quantity we predict, so it is never supplied as an input. We take the natural logarithm of concentration to compress its wide numerical range. We then standardize inputs by subtracting their training-set mean and dividing by their training-set standard deviation. This puts different quantities on comparable numerical scales without claiming they have the same physical effect. Only training data determine those transformations. Because measured total thickness is an input, this is conditional inference from film state, rather than prediction from recipe settings alone.
IF ASKED
Preprocessing includes matching samples, harmonizing units, checking values, and applying transformations. We must confirm the recorded concentration units before giving the fitted relationship a mechanistic interpretation.
TRANSITION
Here is how those inputs pass through the network and how we enforce the physical bound.
TECHNICAL REFERENCE AND SOURCES
Recorded concentration spans 0.02 to 10 in the measured CSV, a 500-fold range. A natural log reduces scale imbalance. The source labels say g/mL, but high values and differences between workbooks and derived tables require lab confirmation. StandardScaler fits the training rows only. Bonded thickness never enters the input set. Total thickness is also the raw output envelope and is required at inference. Solvent descriptors have only three solvent-associated combinations in the synthetic data.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md

## Slide 7
14 Oct 2026
7
Compact network and bounded bonded thickness
3 or 7
inputs
16 + 16
tanh
Bounded
bonded hB
Derivative
penalties
NETWORK DETAILS
Two hidden layers, 16 units each
One output logit
353 parameters with three inputs
417 parameters with seven inputs
Tanh supports second derivatives
PHYSICAL OUTPUT
Raw measured total thickness
defines the output bound
Notes: SPEAKER SCRIPT
The implemented network has two internal layers, with 16 units in each. A unit forms an adjustable combination of its inputs and applies a smooth nonlinear function. Tanh, or hyperbolic tangent, is the smooth function used inside these layers. We chose it because the loss calculation needs second derivatives. In the equation, z represents the standardized inputs, theta represents the adjustable parameters, and f is the network's raw output. The sigmoid function maps that raw output into a fraction between zero and one. Multiplying the fraction by measured total thickness gives predicted bonded thickness. The hat means predicted, B means bonded, and T means total. This construction guarantees a nonnegative prediction no larger than a valid positive total. The model has 353 adjustable parameters with three inputs and 417 with seven inputs.
IF ASKED
The guarantee concerns the allowed range of the prediction. A value can satisfy that range and still be far from the actual bonded thickness. These fitted parameters are not independently identified adsorption constants.
TRANSITION
The output transformation supplies the bound. The following loss terms guide how the model learns within that bound.
TECHNICAL REFERENCE AND SOURCES
Architecture: d inputs, Linear(d,16), tanh, Linear(16,16), tanh, Linear(16,1), then sigmoid multiplied by raw measured total thickness. Parameter count is 16d+16+272+17, giving 353 for d=3 and 417 for d=7. Xavier-uniform weights and zero biases initialize the network. A positive measured total is required in data loading. Finite logits approach the endpoints asymptotically. The standard-NN ablation retains the same hidden layers but uses a linear unbounded output. Diagram structure is reused from slide 15 of the provided reference.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md

## Slide 8
14 Oct 2026
8
Loss terms and initial coefficients
Term | Definition or behavior | Initial coefficient
Data | Mean squared error in bonded thickness Normalize by training target standard deviation | 1
Curvature | Mean squared diagonal second derivative With respect to standardized transformed inputs | 0.001
Monotonicity | Penalize partial derivatives with the wrong sign Separate positive-concentration ablation | 0 default 0.01 ablation
Velocity curvature | Second derivative with respect to measured withdrawal velocity input | 0 in current runs
LLD residual | Compare predicted dry mobile thickness with the eligible hydrodynamic estimate | 0 in current runs
Values are available for all loss terms. Remaining datasets need aggregation and preprocessing
Notes: SPEAKER SCRIPT
The loss combines an error score for each selected objective. The data term penalizes disagreement with measured bonded thickness. The curvature term discourages a highly wavy fitted response. Lambda denotes a coefficient that controls the importance of a penalty relative to data fit. In the reported default PINN runs, the data coefficient is one and the curvature coefficient is 0.001. The separate concentration experiment uses a monotonicity coefficient of 0.01. Velocity curvature and the hydrodynamic residual have zero coefficients in the reported runs, so they do not influence those fits. We have the values required for all of these terms. The remaining datasets still need aggregation and preprocessing before we activate them. A zero coefficient describes what we used in those runs; it does not mean the physical values are unavailable.
IF ASKED
The thickness bound has no coefficient here because the architecture enforces it directly. A weighted penalty can trade off against other errors; a hard output restriction cannot be violated by that tradeoff.
TRANSITION
The next slide gives the mathematical definitions, but the main idea is the behavior each term discourages.
TECHNICAL REFERENCE AND SOURCES
Ldata = mean(((hB_hat-hB)/sy)^2), with sy the population standard deviation of training targets floored at 1e-6. Lsmooth is a diagonal-Hessian curvature prior of hB_hat/sy in standardized/log-transformed coordinates, not a full Hessian norm. Differentiate the total-thickness envelope too. v0.2 evaluates derivative terms on up to 256 deterministic training-row samples per epoch. No arbitrary Cartesian collocation is added. Monotonic penalties are local soft penalties on normalized gradients. Weight decay is an optimizer parameter, separate from the displayed loss. October 14, 2026 project-status clarification from Alexander Adams: values required for all proposed loss terms are available. The remaining datasets require aggregation and preprocessing before these terms can enter training. Their zero weights describe the archived runs, not missing measurements. The LLD residual applies to the mobile layer.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic_monotonic.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py
Project status clarification from Alexander Adams, October 14, 2026

## Slide 9
14 Oct 2026
9
Mathematical definitions of the loss terms
Each loss scores a different kind of error. The coefficients set how strongly training responds to each score.
DATA FIT
Prediction error relative to measured bonded thickness
INPUT SMOOTHNESS
Penalizes curvature in each recorded input
MONOTONICITY
Penalizes slopes that oppose the selected sign
VELOCITY SMOOTHNESS
Penalizes curvature in the standardized velocity input
z: standardized inputs sy: training target scale
n: data rows m: derivative rows d: input count
Notes: SPEAKER SCRIPT
There is no need to read every summation aloud. Each summation averages an error over a set of training rows. The first expression squares the difference between predicted and measured bonded thickness, after scaling by the training target's standard deviation. In the other expressions, q is the scaled prediction and z is a standardized input. A first derivative is the local slope of the prediction as an input changes. A second derivative describes how quickly that slope changes, or curvature. The smoothness term penalizes curvature across input directions. The monotonicity term penalizes slopes with the opposite sign to a selected hypothesis. The velocity term applies curvature penalization specifically to the velocity input. Here, n counts data rows, m counts rows used for derivatives, and d counts input features.
IF ASKED
J is the selected set of monotonic inputs, and s chooses the expected direction for each. These are local, soft penalties. The derivatives are taken in standardized coordinates, so their magnitudes are not raw physical-unit derivatives. Automatic differentiation computes them from the model's mathematical operations, rather than estimating them from noisy neighboring measurements.
TRANSITION
These terms connect to the four physical constraints originally proposed for the project.
TECHNICAL REFERENCE AND SOURCES
The symbols reproduce the implementation exactly. q is predicted bonded thickness divided by s_y, the population standard deviation of training targets with floor 1e-6 nm. n is the count of training data rows, m is the count selected for derivatives (up to 256 per epoch), and d is the number of inputs. z contains standardized transformed predictors, including log concentration. J is the configured set of monotonic features and s_j is their selected direction, positive or negative. z_U is the standardized withdrawal-velocity coordinate; this is not an unscaled SI-velocity derivative. All derivatives include the total-thickness output envelope. Curvature is a diagonal Hessian penalty, not the full Hessian norm. Monotonicity is a soft local penalty. No derivative penalty is evaluated on the held-out test. LaTeX sources for all equations are retained in assets/equations.tex.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py

## Slide 10
14 Oct 2026
10
Status of the four proposed physics constraints
Constraint | Implementation | Current status
Thickness bound | Sigmoid output multiplied by measured total thickness | ACTIVE Hard guarantee
Velocity smoothness | Penalty on velocity curvature | VALUES AVAILABLE Aggregation / preprocessing pending
Monotonic trends | Configurable derivative-sign loss Training-only trend diagnostics | CONCENTRATION TESTED Other terms await data preparation
Hydrodynamic scaling | LLD residual on the dry mobile layer Explicit regime and conversion checks | VALUES AVAILABLE Aggregation / preprocessing pending
Required values are available for every loss term. The remaining datasets still need aggregation and preprocessing before use in training.
Reported runs use data fit and curvature, with a separate concentration ablation
Notes: SPEAKER SCRIPT
This slide separates the proposed constraints from what actually influenced the reported fits. The thickness bound is active by construction. General input curvature is also active in the default PINN loss, although it is not a direct test of withdrawal-velocity smoothness. We separately tested a positive concentration-monotonicity penalty. Velocity curvature and hydrodynamic scaling are implemented, and their required values are available, but their datasets still need aggregation and preprocessing. We should therefore describe them as awaiting data preparation. For the other monotonic relationships, we also need to inspect the prepared data and assess whether a consistent direction is justified. Having a value available does not automatically establish the physical hypothesis. No result shown later should be interpreted as including the currently inactive terms.
TRANSITION
The hydrodynamic term is a useful example of both the physics and the preparation needed before activation.
TECHNICAL REFERENCE AND SOURCES
Status update supplied by Alexander Adams on October 14, 2026: the values required for all proposed loss functions are available. Aggregation and preprocessing of the other datasets remain outstanding. The reported archived runs used data fit and the general curvature prior, plus a separate positive-concentration monotonicity ablation. Velocity curvature and the LLD residual remain off in these runs; this reflects dataset preparation status rather than unavailable measurements. The bound is an output transform, not a weighted loss. The concentration sign remains an exploratory hypothesis, and data availability alone does not validate a causal viscosity relationship or hydrodynamic applicability. The nonnegative mobile layer follows from the bound and is not an independent constraint.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/PHYSICS_CONSTRAINTS.md
Project status clarification from Alexander Adams, October 14, 2026

## Slide 11
14 Oct 2026
11
Hydrodynamic residual and activation requirements
η: viscosity U: withdrawal velocity
γ: surface tension ρ: density
AVAILABLE VALUES
Velocity, solution viscosity, surface tension,
and solution density
Independent wet-to-dry conversion factor
VALIDITY CHECKS
Flat-plate, Newtonian, eligible regime
Explicit per-row applicability flag
Capillary number below 0.01
A: eligible rows fdry: independent dry conversion sy: training target scale
Values are available. Aggregate and preprocess the datasets before enabling this loss
Notes: SPEAKER SCRIPT
LLD refers to Landau-Levich-Derjaguin dip-coating scaling. The capillary number compares viscous effects with surface-tension effects. It combines viscosity, withdrawal velocity, and surface tension. The next expression estimates wet coating thickness for the applicable flat-plate, Newtonian regime. We apply a separately supplied wet-to-dry factor before comparing that estimate with predicted dry mobile thickness. The predicted mobile thickness is total thickness minus predicted bonded thickness. That distinction matters: this residual constrains the mobile layer and does not establish a governing law for bonded adsorption. The needed values are available. We must aggregate matching samples, harmonize units, and preprocess the datasets before using the term. We also check the applicability flag, conversion factor, and capillary-number gate for each eligible row.
IF ASKED
A residual is the mismatch between a model prediction and a physical relation. Only eligible rows enter this residual. The wet-to-dry factor must be independent of the bonded target, so we do not build the answer into the constraint. The small-capillary-number threshold is an initial gate, not a guarantee that every other assumption holds.
TRANSITION
With the architecture and loss defined, here is how the parameters were fitted and how we made the comparisons fair.
TECHNICAL REFERENCE AND SOURCES
The 0.9458 classical plate coefficient is supported by the JFM two-liquid dip-coating paper. U in mm/s converts by 1e-3 to m/s, viscosity cP by 1e-3 to Pa*s, surface tension mN/m by 1e-3 to N/m, and wet thickness m to nm by 1e9. rho is kg/m3 and g=9.81 m/s2. The conversion factor must be independent of the bonded target, positive and <=1. The Ca threshold is a conservative starting gate, not a universal regime guarantee. Geometry, wetting, evaporation and interface validity are supplied by the lab flag. Current runs leave this loss off. October 14, 2026 project-status clarification from Alexander Adams: values required for all proposed loss terms are available. The remaining datasets require aggregation and preprocessing before these terms can enter training. Their zero weights describe the archived runs, not missing measurements. The LLD residual applies to the mobile layer.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/physics.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_measured_physics.example.json
https://www.cambridge.org/core/journals/journal-of-fluid-mechanics/article/dipcoating-flow-in-the-presence-of-two-immiscible-liquids/CB484EB73B1903B5933AB087847C642E
Project status clarification from Alexander Adams, October 14, 2026

## Slide 12
14 Oct 2026
12
Training configuration and matched baselines
Setting | Initial choice
Optimizer | Adam
Learning rate | 0.001
Weight decay | 0.0001
Maximum epochs | 1,500
Validation patience | 150 epochs
Gradient clipping | Norm = 10
Derivative sample | Up to 256 training rows
Initialization | Xavier / zero biases
Reproducibility | Seed 42, CPU
NEURAL COMPARISONS
PINN: hard bound plus curvature regularization.
Bounded NN: same output bound, with physics penalties off.
Standard NN: same hidden layers and optimizer, with a linear output.
TREE BASELINES
RF: 300 trees, minimum leaf size 2
GB: 100 trees, depth 2, learning rate 0.05
Validation chooses neural checkpoints. Fixed tree settings receive no test-driven tuning
Notes: SPEAKER SCRIPT
Adam is the numerical optimizer that adjusts network parameters using the slope of the loss. The learning rate controls the size of those adjustments. An epoch is one training iteration over the full training set in this implementation. We allow up to 1,500 epochs and stop early if validation error does not improve for 150 epochs. Gradient clipping limits unusually large updates, and weight decay discourages unnecessarily large parameter values. A fixed seed controls random initialization and sampling so a run can be reproduced, but one seed does not establish robustness. The bounded network comparison uses the same bound without the physics penalties. The standard network uses the same internal layers with an unrestricted output. Random forest averages many decision trees, while gradient boosting builds a sequence of trees that correct earlier errors.
IF ASKED
A decision tree makes predictions through a sequence of input-based branching rules. Matching data splits and keeping the test out of model selection is more important than making these different model families look architecturally identical.
TRANSITION
The next slide explains what training, validation, and test mean in these experiments.
TECHNICAL REFERENCE AND SOURCES
All neural models use full-batch supervised training, training-only preprocessing and normalized data loss. Adam uses coupled weight decay as implemented by torch.optim.Adam. Torch uses float32 tensors, one CPU thread and deterministic operations. Early stopping counts epochs without validation improvement >1e-7 and restores the selected state. v0.2 experimental PINN selects epoch 76 and stops after epoch 226. Synthetic PINNs select epoch 1500. RF and GB settings are fixed untuned baselines.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config.json
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/core.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/train.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/run_record.json

## Slide 13
14 Oct 2026
13
Evaluation splits and interpretation
Run | Training | Validation | Test
Measured concentration groups | 28 | 12 | 18
Measured high-concentration holdout | 36 | 12 | 10
Synthetic concentration groups | 1,959 | 407 | 442
MEASURED GENERALIZATION
Hold out entire concentration levels.
The extrapolation test reserves
3, 5, 7, and 10 in recorded units.
SYNTHETIC GENERALIZATION
Synthetic parent IDs are unavailable.
Exact concentration grouping cannot
prove independent source experiments.
Compare models within each shared split. Do not compare scores across protocols
Notes: SPEAKER SCRIPT
Training rows determine the adjustable model parameters. Validation rows help select a checkpoint, meaning a saved set of parameters from a particular training stage. Test rows provide the final held-out comparison and do not select the checkpoint. We grouped rows by concentration, so an entire concentration level stays in one partition instead of being spread across training and test. This is a harder and more relevant check than randomly separating nearly identical examples. The high-concentration test asks whether the model can predict beyond the range represented in training. The measured and synthetic studies have different sample counts and distributions, so comparisons should be made within each shared split. Synthetic parent identities remain unresolved, so concentration grouping alone does not prove that the underlying source experiments are independent.
IF ASKED
Data leakage means information that should be reserved for evaluation influences training or selection. Fitting preprocessing only on training rows prevents one common form, but it cannot by itself resolve unknown synthetic ancestry.
TRANSITION
Now we can interpret the first measured-data benchmark.
TECHNICAL REFERENCE AND SOURCES
Grouped split reserves 20% of concentration groups for test and then 20% of remaining groups for validation, so row proportions vary. Extrapolation reserves the largest four of sixteen measured concentration levels. The v0.2 synthetic default and monotonicity runs use identical retained rows and partitions. Existing historical stratified-CV RF scores in the September deck use other protocols and are not direct competitors for these single-split results. True independent batches/specimens should replace concentration as the grouping unit when available.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/train.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/splits.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/splits.csv

## Slide 14
14 Oct 2026
14
Initial measured-data benchmark
58 observations, three inputs, 18 held-out rows
Chart: Held-out RMSE (nm)
| PINN | Bounded | Standard | RF | GB
RMSE (nm) | 0.12225 | 0.12241 | 0.21195 | 0.06698 | 0.064933
Model | RMSE (nm) | R²
PINN | 0.1223 | -0.392
Bounded NN | 0.1224 | -0.395
Standard NN | 0.2119 | -3.183
Random forest | 0.0670 | 0.582
Gradient boosting | 0.0649 | 0.607
PINN MAE: 0.1117 nm. All models: 0% observed bound violations.
Gradient boosting and random forest outperform the initial neural models
Notes: SPEAKER SCRIPT
Every model here predicts the same 18 held-out measured rows. The bars show root mean squared error, or RMSE, in nanometers. It squares each prediction error, averages those squares, and takes the square root, so larger misses receive extra emphasis. Lower bars are better. The PINN is about 0.1223 nanometers, while gradient boosting is about 0.0649 nanometers. The bounded network without the curvature penalty is almost identical to the PINN, so this test does not establish an accuracy benefit from the default penalty. MAE is mean absolute error, the average magnitude of a miss. R-squared compares squared error with predicting the held-out set's own mean. A negative value means worse squared error than that reference. Zero observed bound violations is a separate result from predictive accuracy.
IF ASKED
The tree models also had no observed violations on these test rows, but only the bounded architecture guarantees the range for any valid total. A single small holdout is exploratory evidence, not a stable estimate across independent batches.
TRANSITION
The next test shows particularly clearly why satisfying the bound does not ensure accurate extrapolation.
TECHNICAL REFERENCE AND SOURCES
v0.2 experimental grouped run reproduces the original measured grouped results. Metrics refer only to 18 test observations on held-out concentration levels. PINN MAE 0.111693 nm, RMSE 0.122251 nm, R2 -0.391624. GB MAE 0.055622 nm, RMSE 0.064933 nm, R2 0.607406. All five observed violation fractions are zero, but only bounded outputs guarantee the inequality. Negative R2 means worse than a constant test-set-mean predictor on this small split. This is not evidence that neural models cannot work after a separate validation-based study.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/metrics.csv

## Slide 15
14 Oct 2026
15
Measured high-concentration extrapolation
Chart: Bonded thickness at held-out concentrations
| 3 | 3 | 3 | 5 | 5 | 5 | 7 | 7 | 7 | 10
Observed | 0.55 | 0.56 | 0.57 | 0.56 | 0.55 | 0.55 | 0.5 | 0.53 | 0.52 | 0.51
PINN | 0.56907 | 0.56412 | 0.56814 | 0.72507 | 0.73034 | 0.7443 | 1.31 | 1.2969 | 1.3547 | 1.8387
RF | 0.57942 | 0.5801 | 0.57942 | 0.57942 | 0.5801 | 0.5801 | 0.49937 | 0.49937 | 0.49937 | 0.57092
Model | RMSE (nm)
PINN | 0.6168
Bounded NN | 0.6115
Standard NN | 0.1042
Random forest | 0.0294
Gradient boosting | 0.0296
10 measured test rows
All models have negative R²
PINN R²: −759.817
The PINN satisfies the bound while its error grows at unseen high concentrations
Notes: SPEAKER SCRIPT
The horizontal axis is recorded concentration and the vertical axis is bonded thickness. The symbols compare actual measurements with PINN and random-forest predictions at concentrations reserved for testing. Extrapolation means predicting beyond the training range, where the fitted relationship has less direct support. At the high end, the PINN predictions rise well above the observed bonded thickness. Its RMSE is about 0.617 nanometers, compared with about 0.0294 for random forest. The PINN still remains below total thickness, so the bound works even though the prediction is inaccurate. All models have negative R-squared here. The observed bonded values span a very narrow range, so that metric has a small reference variance and can become extremely negative. We should read it alongside error in nanometers and the actual points.
IF ASKED
The increasing measured total-thickness envelope may contribute when the predicted fraction extrapolates poorly, but we have not established that as the cause. A monotonicity or physics prior must be tested rather than assumed to fix this failure.
TRANSITION
The larger synthetic study answers a different question: how the model fits the represented generated distribution.
TECHNICAL REFERENCE AND SOURCES
Legacy v0.1 extrapolation uses 36 training, 12 validation and 10 test rows. RF RMSE is 0.029366 and R2 -0.724719, GB RMSE 0.029637 and R2 -0.756752. Test bonded values range only 0.50 to 0.57 nm, so R2 is highly sensitive to small error. At recorded concentration 10 the PINN predicts about 1.839 nm for observed 0.51 nm, still below measured total 13.18 nm. Multiplication by increasing total may contribute to error when the learned fraction extrapolates poorly. This is a plausible explanation, not a proven mechanism. No subsequent tuning used this test.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/legacy_initial_extrapolation/predictions.csv

## Slide 16
14 Oct 2026
16
Seven-input synthetic benchmark
2,808 retained rows, seven inputs, 442 held-out rows
Chart: Synthetic holdout RMSE (nm)
| PINN | Bounded | Standard | RF | GB
RMSE (nm) | 0.055718 | 0.055137 | 0.054133 | 0.035903 | 0.074783
Model | RMSE (nm) | R²
PINN | 0.0557 | 0.905
Bounded NN | 0.0551 | 0.907
Standard NN | 0.0541 | 0.911
Random forest | 0.0359 | 0.961
Gradient boosting | 0.0748 | 0.829
PINN MAE: 0.0436 nm. All models: 0% observed bound violations.
Synthetic PINN R² reaches 0.905. Random forest still gives the lowest error
Notes: SPEAKER SCRIPT
This benchmark uses the 2,808 retained synthetic rows, seven inputs, and 442 shared held-out rows. The PINN's RMSE is about 0.0557 nanometers and its R-squared is about 0.905. This indicates a reasonably close fit within this synthetic test distribution. Random forest still has the lowest error, about 0.0359 nanometers. The bounded and standard neural networks are also slightly better than the default PINN on this split, so we still do not have evidence that the curvature term improves accuracy. These results cannot be compared directly with the measured benchmark as an experimental improvement. The data source, feature count, and distribution all changed. Zero observed bound violations again describes these test rows, while the architecture provides the explicit global range restriction for valid totals.
TRANSITION
The parity plots make the individual prediction errors easier to see.
TECHNICAL REFERENCE AND SOURCES
PINN MAE 0.043595 nm, RMSE 0.055718 nm, R2 0.905199. RF MAE 0.020570 nm, RMSE 0.035903 nm, R2 0.960637. This is one synthetic-distribution holdout with seed 42. It cannot be compared as an accuracy improvement over the 58-row measured study because data, feature count, regime composition and test distribution differ. Synthetic siblings and generator statistics may leak without parent provenance. All test violation fractions are zero.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/metrics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 17
14 Oct 2026
17
Synthetic holdout parity: PINN and random forest
Chart: PINN
Ideal prediction | 0.15 | 1.15
Chart: Random forest
Ideal prediction | 0.15 | 1.15
Both plots use all 442 identical test rows and matching axes
Notes: SPEAKER SCRIPT
Each point represents one of the same 442 held-out synthetic rows. Observed bonded thickness is on the horizontal axis and predicted bonded thickness is on the vertical axis. A perfect prediction lies on the diagonal. Points above the line are overpredictions, and points below it are underpredictions. Both panels use matching axes, so we can compare the scatter fairly. The random-forest predictions lie closer to the diagonal overall, consistent with its lower RMSE. The PINN shows a wider spread, especially in parts of the lower and middle range. Overlapping points may hide repeated or very similar synthetic examples. Their density should not be interpreted as an equal number of independent laboratory observations.
IF ASKED
These plots show prediction agreement, not calibrated uncertainty. The spread of points does not give a confidence interval for a new experimental sample.
TRANSITION
We then changed one loss setting to investigate the concentration-monotonicity hypothesis.
TECHNICAL REFERENCE AND SOURCES
Each point is one archived held-out synthetic row. Axes are equal in both panels, from 0.15 to 1.15 nm, and the gray diagonal marks predicted=observed. Repeated or overlapping points are not jittered. The raw dataset contains synthetic replicates, so apparent point density does not indicate independent experimental replication. Random forest predictions lie closer to the diagonal on this run.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/predictions.csv

## Slide 18
14 Oct 2026
18
Concentration-monotonicity ablation
PINN run | RMSE (nm) | R² | Negative local concentration slope
Default curvature prior | 0.055718 | 0.905199 | 43.44%
Positive concentration penalty | 0.056009 | 0.904208 | 40.99%
Chart: Training rows with negative concentration partial derivative
| Pooled | 0.377 cP | 0.423 cP | 0.68 cP
Default | 0.43441 | 0.86553 | 0.23169 | 0.31365
Concentration penalty | 0.4099 | 0.82386 | 0.20628 | 0.30184
The penalty reduces some negative slopes but slightly worsens held-out error
Notes: SPEAKER SCRIPT
An ablation is a controlled comparison in which we change one component while holding the rest fixed. Here we added a penalty against negative concentration slopes. A partial derivative asks how the model changes with concentration while the other model inputs are held fixed. The fraction of training rows with a negative local concentration slope fell from about 43.44 percent to 40.99 percent. That is a modest reduction, rather than a guarantee of monotonic behavior everywhere. Held-out RMSE became slightly worse, from about 0.055718 to 0.056009 nanometers. The bars break the training-gradient diagnostic into viscosity-associated groups. These correlated synthetic solvent groups do not isolate a causal viscosity effect. This experiment therefore tests a hypothesis and does not justify adopting the penalty as the default.
IF ASKED
The slope percentages are training-set diagnostics; they were not estimated by tuning to the test set. A soft local penalty can leave violations and can trade off against data fit.
TRANSITION
The learning curves show another part of the initial testing: how the fitting process evolved over time.
TECHNICAL REFERENCE AND SOURCES
Ablation sets monotonic_weight=.01 and sign +1 on concentration only. Architecture, seed, preprocessing, split and other weights match the default run. Fractions come from training-only gradients, not test data. Default pooled negative fraction .434405, ablation .409903. Cohorts are solvent-associated viscosities .377, .423 and .68 cP. In the .377 cohort the training Spearman association is only .100041. A soft local penalty does not guarantee global monotonicity, and synthetic correlation is not evidence of causal chemistry. Keep this hypothesis separate from the default.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/training_trend_diagnostics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_concentration_monotonic/training_trend_diagnostics.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/config_synthetic_monotonic.json

## Slide 19
14 Oct 2026
19
Training histories and selected checkpoints
Chart: Measured PINN
| 1 | 6 | 11 | 16 | 21 | 26 | 31 | 36 | 41 | 46 | 51 | 56 | 61 | 66 | 71 | 76 | 81 | 86 | 91 | 96 | 101 | 106 | 111 | 116 | 121 | 126 | 131 | 136 | 141 | 146 | 151 | 156 | 161 | 166 | 171 | 176 | 181 | 186 | 191 | 196 | 201 | 206 | 211 | 216 | 221 | 226
Training data loss | 2.8329 | 2.7629 | 2.6793 | 2.5812 | 2.4682 | 2.3391 | 2.1929 | 2.0282 | 1.8431 | 1.634 | 1.3941 | 1.112 | 0.7692 | 0.34929 | -0.059142 | -0.19057 | -0.3231 | -0.54496 | -0.53727 | -0.51981 | -0.57602 | -0.59848 | -0.6224 | -0.64753 | -0.6558 | -0.66734 | -0.68086 | -0.69128 | -0.70185 | -0.7111 | -0.71964 | -0.72854 | -0.73709 | -0.7453 | -0.75314 | -0.76056 | -0.76768 | -0.77446 | -0.78092 | -0.7871 | -0.79303 | -0.79874 | -0.80421 | -0.80944 | -0.81442 | -0.81917
Validation data loss | 3.0567 | 3.0069 | 2.9467 | 2.8746 | 2.7894 | 2.6892 | 2.5717 | 2.4334 | 2.2696 | 2.0738 | 1.8375 | 1.5488 | 1.188 | 0.72026 | 0.14791 | -0.095871 | -0.055884 | 0.11097 | 0.28341 | 0.29304 | 0.21353 | 0.15589 | 0.14449 | 0.15743 | 0.1578 | 0.13175 | 0.10198 | 0.089863 | 0.09382 | 0.099395 | 0.096012 | 0.085313 | 0.074578 | 0.067259 | 0.061684 | 0.055321 | 0.048109 | 0.041601 | 0.036434 | 0.031761 | 0.026596 | 0.020911 | 0.015315 | 0.010168 | 0.0053384 | 0.00059528
Chart: Synthetic PINN
Selected epoch 76
Training stopped at epoch 226
Selected epoch 1,500
Training reached the configured limit
A validation-based optimization-budget study remains a next step
Notes: SPEAKER SCRIPT
The horizontal axis counts epochs, or repeated full-training-set optimization steps. The vertical axis shows the base-ten logarithm of normalized mean squared error. The logarithm lets us see large early errors and smaller later errors on the same plot. A vertical value of zero corresponds to normalized error one, and minus one corresponds to 0.1, so a decrease of one unit means a tenfold reduction. The blue line is training error and the gold line is validation error on rows not used for parameter updates. In the measured run, validation selected epoch 76 and patience stopped training at 226. In the synthetic run, the selected checkpoint was the final allowed epoch, 1,500. That motivates a validation-based study of the optimization budget; it does not promise better test performance from longer training.
IF ASKED
Different runs normalize by different training target scales, so these plots describe optimization within each run rather than comparing absolute nanometer accuracy across datasets. A training-validation gap can suggest overfitting, but the plot alone does not establish a single cause.
TRANSITION
These diagnostics also guide which architecture changes are worth trying next.
TECHNICAL REFERENCE AND SOURCES
Charts use log10 of archived normalized data-loss and validation-loss histories. Log display retains the full initial and final loss ranges without clipping. A value of -1 means normalized MSE=0.1, 0 means 1, and 3 means 1000. The normalization uses each run training target standard deviation, so charts describe within-run optimization rather than comparing absolute nm errors across datasets. Figure samples every fifth measured epoch and every 25th synthetic epoch plus endpoints. All three synthetic neural models selected epoch 1500. Test results never select epochs.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_experimental_grouped/pinn_history.csv
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/runs/v020_synthetic_grouped/pinn_history.csv

## Slide 20
14 Oct 2026
20
Architecture choices from the literature
Architecture | Relevant work | Decision for this project
Compact tanh MLP | Raissi et al., 2019 | Initial backbone for differentiable small-data constrained regression
Modified or gated MLP | Wang et al., 2021 Gradient pathologies | Next candidate if diagnostics show conflicting loss gradients
Fourier-feature PINN | Wang et al., 2021 Eigenvector bias | Test only with evidence of multiscale response rather than measurement noise
Bayesian PINN | Yang et al., 2021 B-PINNs | Consider after auditing replicate noise and checking uncertainty calibration
DeepONet / FNO | Lu et al., 2021 Li et al., ICLR 2021 | Defer until trajectories, profiles, or families of field solutions exist
The current scalar table supports a compact network before operator-learning models
Notes: SPEAKER SCRIPT
An architecture specifies how the model's mathematical operations are connected. Our initial choice is a compact multilayer perceptron, or MLP, which maps a short list of numerical inputs to a scalar prediction. Tanh makes it smooth enough for the derivative penalties. More elaborate choices address specific problems. A modified or gated MLP can help when different loss terms produce competing training gradients. Fourier features add sinusoidal representations that can describe variation at different scales, but could also fit noise without sufficient evidence. A Bayesian PINN represents uncertainty in fitted quantities, which still requires checking that uncertainty against measurements. DeepONet and Fourier Neural Operator learn mappings between functions or fields. Our present table contains scalar inputs and outputs, so those operator models are not the immediate next step.
IF ASKED
The literature motivates candidate methods; it does not establish an adsorption law for this material system. We should choose added complexity in response to a demonstrated failure and evaluate it on the same protected test structure.
TRANSITION
To make those comparisons meaningful, each experiment needs a clear record.
TECHNICAL REFERENCE AND SOURCES
Literature is methodological background rather than evidence of a PDMS adsorption law. The sigmoid envelope is our algebraic project parameterization, not a reproduction of Lu et al. hPINN augmented-Lagrangian optimization. Operator architectures need function-valued input/output structure absent from three/seven scalar predictors. Full verified source links appear on the reference slide and in the repository literature review.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/LITERATURE_REVIEW.md
https://doi.org/10.1016/j.jcp.2018.10.045
https://arxiv.org/abs/2001.04536
https://arxiv.org/abs/2012.10047
https://arxiv.org/abs/2003.06097
https://www.nature.com/articles/s42256-021-00302-5
https://arxiv.org/abs/2010.08895

## Slide 21
14 Oct 2026
21
Recorded experiments and reproducibility
Run | Version | Start, Oct 11 (EDT) | PINN RMSE
Measured grouped baseline | 0.1.0 | Unknown legacy time | 0.122251 nm
Measured extrapolation | 0.1.0 | Unknown legacy time | 0.616773 nm
Synthetic grouped benchmark | 0.2.0 | 11:42:34 | 0.055718 nm
Measured grouped rerun | 0.2.0 | 11:44:41 | 0.122251 nm
Synthetic concentration ablation | 0.2.0 | 11:45:28 | 0.056009 nm
Each new run stores execution times, per-model settings and results, exact source/configuration, data and artifact hashes, split IDs, and saved checkpoints.
Ten integrity tests passed. All 111 archived artifacts match their published Git bytes
Notes: SPEAKER SCRIPT
Each row identifies a distinct archived experiment, including the implementation version and its PINN result. The newer runs record execution times prospectively. The older runs did not record those times, so they remain unknown instead of being reconstructed from file modification dates. Reproducibility also needs more than a timestamp. We preserve the exact settings, source snapshot, data identity, partition membership, predictions, and selected checkpoint. A checkpoint is the saved set of learned network parameters. A hash is a compact digital fingerprint that changes if the underlying bytes change. The integrity checks confirm consistency of the saved artifacts with the published versions. They help us reproduce and audit the experiment; they do not prove the physical hypothesis or scientific conclusion.
TRANSITION
Putting the results together, here is what we can and cannot conclude at this stage.
TECHNICAL REFERENCE AND SOURCES
Legacy start/end execution times were never recorded. Their file modification times are approximate archival evidence and are not presented as execution timestamps. Three v0.2 runs capture UTC and America/New_York times prospectively. Code version plus exact source hash and source snapshot is authoritative when the worktree differed from its Git base. The v0.2 Git-status path-scope bug was corrected and annotated without changing scientific results. Byte-preserving attributes and a later Git renormalization repair preserve archive hashes. Source, models, raw/processed identity, predictions and runs are published on branch codex/pinn-physics-and-run-tracking, draft PR #6. Future runs record automatically but require a commit/push to publish.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/run_tracking.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/verify_runs.py
https://github.com/aadams2006/Pitt-ML-MSE-Project/pull/6

## Slide 22
14 Oct 2026
22
What initial testing establishes
SUPPORTED FINDINGS
The bounded architecture guarantees physically valid thickness predictions for valid totals.
The measured PINN trails tree models on the initial concentration-group holdout.
The synthetic PINN fits the represented distribution, while random forest remains stronger.
LIMITS ON INTERPRETATION
Total thickness is a measured input. Recipe-only prediction needs a separate model design.
Synthetic parent provenance and independent experimental batches remain unresolved.
No calibrated uncertainty, governing PDE, or identified adsorption mechanism is established.
Physics plausibility and predictive accuracy require separate evidence
Notes: SPEAKER SCRIPT
The bounded output construction guarantees a physically allowed thickness range for valid total-thickness inputs. That is a useful property, but it is different from predictive accuracy. On the current measured holdout, the tree baselines outperform the PINN. On the synthetic holdout, the PINN fits the represented distribution, but random forest remains stronger. The current model also uses measured film-state information, including total thickness, so it is not yet a recipe-only predictor. Independent experimental batches and synthetic parent identities still matter for evaluating generalization, meaning performance on genuinely new cases. We have not established calibrated uncertainty, a governing adsorption equation, or a causal mechanism. Finally, the additional loss values are available, but those datasets still need aggregation and preprocessing before we can report their effect.
TRANSITION
The next steps focus first on preparing those available data, then on testing whether each additional loss improves measured-data predictions.
TECHNICAL REFERENCE AND SOURCES
These are single-seed, single-split exploratory tests. Test-set concentration ranges, solvent combinations, independent replicate count, source-unit ambiguity and target algebraic coupling limit causal and deployment claims. The high-concentration test demonstrates that staying within a bound does not ensure accurate extrapolation. No accuracy benefit from default curvature or the tested positive monotonicity penalty is established here.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/INITIAL_RESULTS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md

## Slide 23
14 Oct 2026
23
Next experiments and decision criteria
Workstream | Next action | Evidence to proceed
Data preparation | Aggregate the available datasets Align sample IDs, units and feature fields | Prepared tables with traceable sample matches
Remaining losses | Preprocess available physics values Check regime and dry conversion, then enable | Validated inputs and loss-by-loss ablations
Validation | Repeat seeds and grouped experimental CV Reserve new independent test experiments | Stable error on an untouched measured test
Architecture and losses | Test compact adsorption or saturation priors Tune only on training/validation | Gain over bounded NN with a frozen test
Data efficiency | Augment after splitting measured parents Use fixed measured-test learning curves | Gain on measured tests with known training parents
Immediate priority: aggregate and preprocess the available data for the remaining losses
Notes: SPEAKER SCRIPT
Our immediate priority is to aggregate the available datasets and make the quantities consistent across matched samples. That means aligning sample identities, confirming units, checking values and timing, and producing model-ready tables. We can then preprocess the available physics inputs, verify the applicability conditions, and enable the remaining loss terms one at a time. That controlled sequence lets us identify which term contributes to a change. We should also repeat random seeds and use grouped cross-validation, which rotates independent groups through held-out roles to assess stability. New independent experiments should remain reserved as a final test. If we study synthetic augmentation, we must split the measured parents before generating training examples. The decision criterion is improved performance on protected measured tests, rather than only a lower training loss or a better synthetic score.
IF ASKED
Available measurements do not remove the need for preprocessing or applicability checks. The current holdout results are already exploratory, so repeated model decisions should ultimately be assessed on fresh independent data.
TRANSITION
The final slide lists the methodological references and the repository containing the evidence behind this update.
TECHNICAL REFERENCE AND SOURCES
Alexander Adams confirmed on October 14, 2026 that values for all loss functions are available. The immediate task is to aggregate the datasets, align sample identities, harmonize units and preprocess the values into model-ready tables. Then validate applicability and run controlled loss-by-loss ablations on shared splits. Availability does not imply these terms were used in the archived runs or that their effect on accuracy is established. No new numerical result is promised here. Proposed saturation or adsorption parameterizations still need physical evidence and identifiability checks. Split measured experiments before generating synthetic training rows and keep the test frozen during tuning.
Sources:
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/DESIGN_DECISIONS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/PHYSICS_CONSTRAINTS.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/SYNTHETIC_BENCHMARK.md
Project status clarification from Alexander Adams, October 14, 2026

## Slide 24
14 Oct 2026
24
References and archived evidence
PHYSICS-INFORMED ARCHITECTURES
Raissi, Perdikaris & Karniadakis (2019)
Physics-informed neural networks, JCP
DOI: 10.1016/j.jcp.2018.10.045
Lu et al. (2021)
Hard constraints for inverse design
arXiv: 2102.04626
Wang, Teng & Perdikaris (2021)
Gradient flow pathologies in PINNs
DOI: 10.1137/20M1318043
Wang, Wang & Perdikaris (2021)
Fourier-feature eigenvector bias
DOI: 10.1016/j.cma.2021.113938
Yang, Meng & Karniadakis (2021)
B-PINNs for noisy forward/inverse problems
DOI: 10.1016/j.jcp.2020.109913
Lu et al. (2021)
DeepONet, Nature Machine Intelligence
DOI: 10.1038/s42256-021-00302-5
Li et al. (ICLR 2021)
Fourier Neural Operator
arXiv: 2010.08895
CODE AND RESULTS
GitHub: aadams2006 / Pitt-ML-MSE-Project
PINN folder and experiment register
Draft pull request #6
Results through October 11, 2026. Full sources and numerical details are in speaker notes.
Notes: SPEAKER SCRIPT
These papers provide background for physics-informed learning, hard constraints, training difficulties, and possible alternative architectures. They are methodological references, rather than evidence that a particular bonded-thickness mechanism applies here. The repository contains the implementation, design decisions, data audit, experiment register, and archived numerical outputs used in the figures. The results shown are through October 11, with the October 14 clarification that all proposed loss values are available and the remaining datasets need aggregation and preprocessing. For discussion, the main near-term decision is how to combine and validate those datasets before comparing the additional losses on consistent splits.
TECHNICAL REFERENCE AND SOURCES
Architecture citations are the reviewed papers, not newly generated research claims. The deck uses the five archived PINN runs and the requested reference theme. The classical LLD coefficient and applicability discussion are sourced on slide 9. Data, code, run manifests and predictions identify all quantitative figures. Meeting date: October 14, 2026. Result cutoff: October 11, 2026.
Sources:
https://doi.org/10.1016/j.jcp.2018.10.045
https://arxiv.org/abs/2102.04626
https://doi.org/10.1137/20M1318043
https://doi.org/10.1016/j.cma.2021.113938
https://doi.org/10.1016/j.jcp.2020.109913
https://www.nature.com/articles/s42256-021-00302-5
https://arxiv.org/abs/2010.08895
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/LITERATURE_REVIEW.md
https://github.com/aadams2006/Pitt-ML-MSE-Project/tree/c771a486fe82b1ea13e7a70e156f64f01db03128/PINN/RUN_LOG.md